## Slide 1
LEARN JAVA + ROBOT PROGRAMMING
LESSON 3
Telemetry
Plot position and velocity, live
WPILib 2027 Alpha · Commands V3
Notes: So far the conversation with the motor has been one-way — you talk, it spins. This lesson makes it talk back: a TalonFX has a built-in encoder that reports position and velocity for free, and the theme of the whole lesson is asking instead of telling.

## Slide 2
THE GOAL
Make the motor talk back
Read the drive motor's built-in sensor, log its position and velocity, and watch them plotted live as you drive.
NEW JAVA CONCEPTS
Methods that return values you act on
Chaining calls
Method references (this::logTelemetry)
instanceof pattern matching
NEW ROBOT CONCEPTS
The TalonFX integrated encoder
Logging with Telemetry
Plotting in AdvantageScope
Reacting to scheduler events, not polling
LEARN JAVA + ROBOT PROGRAMMING · TELEMETRY
2
Notes: A TalonFX's built-in encoder gives you position — how many rotations the motor has turned since boot — and velocity, how fast it's turning right now in rotations per second. You read these instead of setting them, which is the "questions vs. actions" split the rest of the lesson builds on.

## Slide 3
SECTION 1 · THE ENCODER
Three dots, three method calls, one chain
Nothing to add yet — this is how you'll read them, in section 4
double rotations = m_driveMotor.getPosition().getValue().in(Rotations);
double rps = m_driveMotor.getVelocity().getValue().in(RotationsPerSecond);
getPosition() returns a signal object, not a plain number.
.getValue() reads a measurement that remembers its own unit; .in(Rotations) says which unit you want it as. Whatever a method returns, you can call methods on it immediately — that's chaining.
LEARN JAVA + ROBOT PROGRAMMING · TELEMETRY
3
Notes: Walk the chain left to right like a little assembly line. m_driveMotor.getPosition() doesn't return a plain number — it returns a signal object, Phoenix's wrapper that carries the value together with a timestamp. .getValue() reads the signal's current value, but that's a measurement that remembers its own unit, so it can't be silently misread as the wrong one. .in(Rotations) is where you say which unit you want it as. This is also a good moment to name a pattern already in use without a name: setThrottle(0.3) is an action — nothing comes back — while getPosition() is a question, and the answer comes back as a return value to catch in a variable. From this lesson on, question-methods start doing the heavy lifting.

## Slide 4
SECTION 2 · TELEMETRY
The name is the address
Nothing to add — just the general shape
Telemetry.log("DriveModule/PositionRotations", rotations);
Every value goes under an organized name, one branch per mechanism.
A hundred values from now, you can still find the one you want. Names carry their units too — PositionRotations, not Position — so nobody has to guess what a number means later.
LEARN JAVA + ROBOT PROGRAMMING · TELEMETRY
4
Notes: Your code runs on the robot; you're looking at a laptop. Telemetry.log("some name", value) is the plumbing that gets a number from one to the other, live. This course holds a standard from day one: the name is the address. Every value goes under an organized name, one branch per mechanism, so a hundred values from now you can still find the one you want — and names carry their units too, PositionRotations rather than just Position, so nobody has to guess what a number means later.

## Slide 5
SECTION 3 · ROBOT.JAVA
Every published value, saved automatically
Edit Robot.java's constructor
public Robot() {
DataLogManager.start(); // saves every published value to a .wpilog file
}
The logger runs before anything else is set up — top of the constructor.
On a real robot the file lands on SystemCore; in sim it lands in a logs/ folder in your project. A session you can scrub through later is how you answer "what just happened?" without making it happen again.
LEARN JAVA + ROBOT PROGRAMMING · TELEMETRY
5
Notes: Telemetry's values are live — visible while the robot runs, gone the instant it stops — unless something is also saving them. DataLogManager.start() does exactly that: start it once, and every value published anywhere gets mirrored into a .wpilog file automatically. It has to go at the very top of the Robot constructor, before anything else gets set up. Recording sim sessions might sound like overkill, but it isn't — a session you can scrub through afterward is how you answer "wait, what just happened?" without having to make it happen again.

## Slide 6
SECTION 4 · DRIVEMODULE.JAVA
A standing callback, not a one-off poll
Edit DriveModule's constructor
public DriveModule() {
Scheduler.getDefault().addPeriodic(this::logTelemetry);
}
private void logTelemetry() {
double rotations = m_driveMotor.getPosition().getValue().in(Rotations);
double rps = m_driveMotor.getVelocity().getValue().in(RotationsPerSecond);
Telemetry.log("DriveModule/PositionRotations", rotations);
Telemetry.log("DriveModule/VelocityRotPerSec", rps);
}
this::logTelemetry is a method reference — shorthand for () -> this.logTelemetry(). addPeriodic runs it every tick, forever, with no command required.
LEARN JAVA + ROBOT PROGRAMMING · TELEMETRY
6
Notes: You want telemetry fresh always, not just while some command happens to be running — that means it belongs somewhere that always runs, on its own schedule, independent of whatever command is currently active. Scheduler.getDefault().addPeriodic(...) registers a callback that runs every tick, forever, for as long as the robot runs, no command required. this::logTelemetry is a method reference — shorthand for () -> this.logTelemetry() — reads naturally out loud as "add a periodic task, this dot logTelemetry." The slash in the dashboard key isn't decoration; it builds a folder tree, and the organization rule for this whole course is that every value a mechanism logs starts with the mechanism's name and a slash. When this robot grows to four modules, a gyro, and an arm, that tree is what keeps a hundred values findable. Worth calling out the standing habit: log from a steady, always-running callback like this one, not from inside command bodies — commands come and go, this callback doesn't, so plots never go blank just because a command ended.

## Slide 7
SECTION 5 · ADVANTAGESCOPE
Watch it plotted, live
1
File → Connect to Simulator
On a real robot it's Connect to Robot, with your team number.
2
NetworkTables → Telemetry → DriveModule
Your folder tree, with both values ticking.
3
Drag VelocityRotPerSec onto the Line Graph tab
A live plot appears.
4
Drag PositionRotations on too, right axis
Two signals, one time axis.
5
Drive, and watch
The traces sit nearly flat — nothing's actually spinning yet. Lesson 4 fixes that.
LEARN JAVA + ROBOT PROGRAMMING · TELEMETRY
7
Notes: AdvantageScope ships in the WPILib installer, so it's already there — it plots live data, overlays signals, scrubs back through time, and opens .wpilog flight-recorder files. Don't be discouraged when the traces sit nearly flat even at full stick — in simulation the motor isn't actually turning yet, so there's nothing for the encoder to count. That's exactly what Lesson 4 fixes. What's built today is the pipe; next lesson gives it something real to carry. On a real robot these plots already work — spin the wheel by hand and watch position climb. And sim or real, DataLogManager has been saving every value to a .wpilog file this whole time; open one with File → Open Log(s) to scrub back through an entire session. This tool comes back constantly — tuning P control in Lesson 5, comparing commanded vs. actual speed, eventually watching the robot drive around a virtual field.

## Slide 8
SECTION 6 · ROBOT.JAVA
Told, not asked
Edit Robot's constructor — add the listener
public Robot() {
DataLogManager.start(); // saves every published value to a .wpilog file
Scheduler.getDefault().addEventListener(this::logCommandStart); // ← added
}
Replace logRunningCommand() with
private void logCommandStart(SchedulerEvent event) {
if (event instanceof SchedulerEvent.Scheduled scheduled
&& scheduled.command().requires(module)) {
Telemetry.log("DriveModule/CurrentCommand", scheduled.command().name());
}
}
Is this a Scheduled event? Type it as one, right there — that's pattern matching. The old version polled and got lucky every time; this one is told.
LEARN JAVA + ROBOT PROGRAMMING · TELEMETRY
8
Notes: Lesson 1's logRunningCommand() asked the scheduler a question every tick and read entry zero off the answer — it worked because every command built so far either parks or loops until canceled, so there's always something running whenever you ask. That guarantee won't last: later lessons build commands that finish on their own, and Lesson 8 ships one that can finish the instant it's scheduled, before a poll ever gets a chance to see it run — asking at just the wrong moment means reading past the end of an empty list, not a stale answer. The fix isn't a smarter poll, it's not polling at all: the scheduler announces every SchedulerEvent it fires — scheduled, completed, canceled, interrupted, and a few more — and addEventListener reacts the instant one happens. Another method reference here, the same shorthand as this::logTelemetry back in section 4, just pointing at a different method. The if line does two jobs at once: "event instanceof SchedulerEvent.Scheduled scheduled" asks whether this event is specifically a Scheduled event, and if so hands it back as a variable named scheduled, typed as that specific kind rather than the general SchedulerEvent — which is why the check has to come first, since only the specific kind has a .command() on it. The && after it can use scheduled right away because Java only evaluates the rest of the line once the left side has already passed. scheduled.command().requires(module) matters because the same event stream fires for every mechanism on the robot, not just this one. Run it again and press the button: DriveModule/CurrentCommand still flips the same way as before — what changed is that it isn't asking anymore, it's told.

## Slide 9
SECTION 6 CONTINUED · ROBOT.JAVA
The command log takes care of itself now
Edit Robot's robotPeriodic(), dropping the call to the old method
@Override
public void robotPeriodic() {
Scheduler.getDefault().run();
}
Ticking the scheduler is still the only thing that has to happen every tick.
Remove the now-unused imports (java.util.List and org.wpilib.command3.Command — nothing here needs them anymore) and add org.wpilib.command3.SchedulerEvent. What changed is how Robot knows what's running, not what shows up on the dashboard.
LEARN JAVA + ROBOT PROGRAMMING · TELEMETRY
9
Notes: logRunningCommand() is gone, and with it the only thing robotPeriodic() needs to do every tick is the scheduler tick itself — the command log takes care of itself now, reacting to events instead of being asked. Run it again and press the button: DriveModule/CurrentCommand on the dashboard still flips between "DriveModule[IDLE]" and "Drive At Speed", exactly like before. What changed is how it knows — the old version asked, every tick, and got lucky every time because nothing could finish between one ask and the next; the new version can't get unlucky, because it isn't asking anymore, it's told, the instant something happens, no matter how briefly "happens" lasts. Worth naming as a callout: Scheduled isn't the only kind of SchedulerEvent — there's a Completed for when a command finishes on its own, Canceled and Interrupted for the other two ways a command's life can end, and a couple more besides. Only one piece of that vocabulary got used here.

## Slide 10
BEFORE YOU MOVE ON
Try it
1
Log the commanded speed
WRITE CODE
Inside driveWithJoystick's loop, log CommandedOutput right where it's computed.
2
Add getPositionRotations()
WRITE CODE
A reading method returning position as a double — safe to share, unlike a command.
3
Rename a dashboard key
Swap "DriveModule/" for "Elevator/", rebuild, and watch a new folder appear in the tree.
4
Log when a command completes
WRITE CODE
Handle SchedulerEvent.Completed and write LastCompletedCommand.
LEARN JAVA + ROBOT PROGRAMMING · TELEMETRY
10
Notes: Logging the commanded speed is a refinement of the always-running rule from section 4: a value that only exists inside a command — like the command's own output — gets logged right where it's computed, not from a periodic callback. On a real robot, overlaying CommandedOutput against VelocityRotPerSec shows how the motor lags the command — the seed of understanding control, which pays off starting in Lesson 5. getPositionRotations() is worth calling out as exposing a reading method alongside command factories — that's fine, readings are safe to share, unlike commands. Renaming a dashboard key is a hands-on demonstration that the slash really is a folder path and the name really is the address — the old entry goes stale and a new folder appears in the tree. The SchedulerEvent.Completed exercise previews the vocabulary callout: Scheduled isn't the only kind of event.

## Slide 11
WHAT YOU LEARNED
Asking instead of telling
Methods split into actions (setThrottle) and questions (getPosition) — chain a question's return value straight into the next call.
Telemetry.log("Mechanism/Name", value) with DataLogManager recording started, is this course's whole telemetry story.
A listener reacting to a SchedulerEvent can't get unlucky the way a poll can — it's told the instant something happens.
NEXT
Lesson 4
Simulation
Give the simulated motor a physics model, so the plots actually respond.
LEARN JAVA + ROBOT PROGRAMMING · TELEMETRY
11
Notes: That naming discipline — Mechanism/Name — feels like overkill for two values; it stops being overkill around value twenty, and this course gets there sooner than it seems. The bigger shift is trading a poll for a listener: logRunningCommand() asked a question every tick and happened to always have an answer, but "happened to" isn't a guarantee. logCommandStart() doesn't ask at all — it registers once and reacts exactly when a SchedulerEvent.Scheduled actually occurs, unpacked with instanceof pattern matching. Same dashboard key, same string showing up, but nothing left that can come up empty. The plots look unimpressive while the sim motor stands still, but Lesson 4 turns the physics on, and these same plots come alive.