## Slide 1
LEARN JAVA + ROBOT PROGRAMMING
LESSON 17
B-Line Autos
A path is a shape on the field, and the robot chases it
WPILib 2027 Alpha · Commands V3 · BLine 2027.0.0-beta.1
Notes: Lesson 9's autonomous was a script: drive a meter, turn, drive a meter. Today it becomes a path — points in field coordinates, drawn on a picture of the field, saved in a file you can redraw between matches — and the robot's job changes from "perform these moves in order" to "find the nearest point on that shape and chase it." That only works because Lesson 14 gave the robot a fused estimate of where it is, so this is where three lessons of localization work finally pay off.

## Slide 2
THE GOAL
Retire the script, follow a drawn path
Replace hand-composed drive-turn-drive autos with a real path — drawn as points on a picture of the field, saved as a file, and followed continuously against Lesson 14's fused pose — with one autonomous opmode per path.
NEW JAVA CONCEPTS
PIDController — the class behind the P control you've written by hand
Method references as actions, not just values
The deploy folder — files the robot reads, not code
NEW ROBOT CONCEPTS
B-Line's path model: straight segments
Three loops at once
Speed limits are physics — can it stop?
Event markers along a path
An opmode is built when it's selected
LEARN JAVA + ROBOT PROGRAMMING · B-LINE AUTOS
2
Notes: B-Line's path model is a chain of Waypoints, TranslationTargets and RotationTargets, connected by straight lines rather than curves. Following a path is three separate control loops at once — distance-to-go, heading, and drift off the line. The speed limits in the path's config file aren't taste: whether the robot can stop where you asked is arithmetic you can do before it ever moves. Event markers fire an action partway along a path. And an opmode is built the moment it's selected, so an auto's path file is read — and, in the simulator, the robot set down at its start — while the robot is still disabled.

## Slide 3
SECTION 1 · WHAT DRIVE-TURN-DRIVE CAN'T DO
A script of nudges, with no idea where it is
Nothing to add — this is code you already have (Autos.driveTurnDrive)
return Command.noRequirements(coroutine -> {
coroutine.await(drivetrain.driveDistance(1.0)); // step 1: forward 1 meter
coroutine.await(drivetrain.turnToHeading(90)); // step 2: face 90°
coroutine.await(drivetrain.driveDistance(1.0)); // step 3: forward 1 meter
})
.named("Drive Turn Drive");
Errors don't cancel — they stack
Each step starts wherever the last one ended. Bump the robot at the start and every step after it is wrong by that much, with nothing in the code that could notice.
LEARN JAVA + ROBOT PROGRAMMING · B-LINE AUTOS
3
Notes: That's a script, and it works. But notice what it doesn't contain: any mention of where the robot is on the field. It's a sequence of relative nudges — go forward a bit, spin, go forward a bit. It's also stuck driving in straight lines and turning in place, because that's all driveDistance and turnToHeading know how to do. Lesson 10 gave this chassis the ability to translate and rotate simultaneously — full swerve freedom — and the autos have never once used it.

## Slide 4
SECTION 1 · THE WHOLE LESSON
A path isn't a list of moves — it's a shape
The robot's job: chase the nearest point on the shape, continuously
Drift off the line, for any reason, and the follower simply drives back. It doesn't need to know why you were off — it only needs to know where you are, which Lesson 14 gave you.
B-Line connects points with straight lines
No curves fitted through your points: corners get rounded by handing off to the next segment early. Less elegant than splines, and much easier to reason about.
LEARN JAVA + ROBOT PROGRAMMING · B-LINE AUTOS
4
Notes: That reframing is what makes the fused pose from Lesson 14 finally pay off. If you know where you are — really know, gyro and wheels and cameras all folded together — then "am I on the line?" is a question you can answer fifty times a second and fix. Most path libraries fit smooth splines through your points; B-Line connects them with lines and rounds the corners by handing off to the next segment early. You can look at a drawn path and know what the robot will do.

## Slide 5
SECTION 2 · INSTALL BLINE
Installed by URL, like LimelightLib
1
Ctrl+Shift+P → WPILib: Manage Vendor Libraries
Then Install new library (online) — BLine isn't in the search list.
2
Paste the URL below
It installs BLine-Lib-2027.json, the build for Commands V3.
3
Rebuild: ./gradlew build
A BLine-Lib.json in vendordeps is the 2026 build — remove it.
Paste into the dialog as ONE line
https://raw.githubusercontent.com/edanliahovetsky/BLine-Lib/
d9967810725ff861767ccde5c5d84981b9defc94/BLine-Lib-2027.json
That long URL names the commit tagged 2027.0.0-beta.1. A commit can't change.
LEARN JAVA + ROBOT PROGRAMMING · B-LINE AUTOS
5
Notes: Same ritual as Lesson 15's LimelightLib: BLine isn't in WPILib's online search list, so you install it by URL. The long URL names one exact commit, the one BLine tagged as its 2027.0.0-beta.1 release, for the same reason as Lesson 15's: BLine's own docs hand out a shorter link that follows whatever they publish next. The file it installs is BLine-Lib-2027.json — the 2027 build, written for this framework's Commands V3. BLine's 2026 build is a different file for a different command framework.

## Slide 6
SECTION 2 · ONE THING THAT WILL LOOK WRONG
BLine lives under frc.robot.lib.BLine
Not your code, even though the package says frc.robot
Every other library announced itself with a vendor's name — com.ctre.phoenix6, com.limelightvision. BLine chose frc.robot.lib.BLine. Unusual, not a mistake: it still comes from the jar.
Four packages you'll import from
.commands (FollowPath) · .path (Path) · .following (DriveType) · .field (FlippingUtil)
LEARN JAVA + ROBOT PROGRAMMING · B-LINE AUTOS
6
Notes: BLine's classes live in packages under frc.robot.lib.BLine — frc.robot.lib.BLine.commands, frc.robot.lib.BLine.path, and a couple of others. So when you type import frc.robot.lib.BLine.path.Path; and it resolves to something you never wrote — in a package that isn't even your first.robot — that's not a mistake. It's just an unusual packaging choice, and it still comes from the jar.

## Slide 7
SECTION 3 · DRIVETRAIN.JAVA
Two new doors: read the motion, command a motion
Add to Drivetrain, below getModulePositions
/**
* How the chassis is moving right now, robot-relative — kinematics run
* backward: four measured wheel velocities in, one chassis motion out.
*/
public ChassisVelocities getChassisVelocities() {
SwerveModuleVelocity[] wheels = new SwerveModuleVelocity[m_modules.length];
for (int i = 0; i < m_modules.length; i++) {
wheels[i] = new SwerveModuleVelocity(
m_modules[i].getDriveVelocityMetersPerSec(),
Rotation2d.fromDegrees(m_modules[i].getSteerAngleDegrees()));
}
return m_kinematics.toChassisVelocities(wheels);
}
/** Drive one tick from a robot-relative chassis motion. The door BLine drives through. */
public void driveRobotRelative(ChassisVelocities speeds) {
applyChassisSpeeds(speeds);
}
LEARN JAVA + ROBOT PROGRAMMING · B-LINE AUTOS
7
Notes: B-Line drives your robot the same way a human driver does: it looks at where you are, decides on a chassis motion, and hands it over. So it needs two things from Drivetrain that aren't public yet. You've already written the reading half: Lesson 16's simulateChassis asked the kinematics the question backward — here are the four wheel velocities I'm measuring, what single chassis motion would produce them? Two callers now want the same answer, so it moves into its own method — the same "pull out a helper" move as Lesson 8's commandRotation. Both go with the other public accessors — getKinematics, getRotation, getModulePositions.

## Slide 8
SECTION 3 · DRIVETRAIN.JAVA
simulateChassis now asks the new method
Then replace the body of simulateChassis below the null check
/** Moves the simulated chassis the way its wheels actually turned this tick. Sim only. */
private void simulateChassis() {
if (m_chassisSim == null) {
return; // a real robot moves itself
}
m_chassisSim.update(getChassisVelocities(), 0.020);
}
A door punched on purpose, for one caller
applyChassisSpeeds stays private. driveRobotRelative is a narrow public door with a name that says who it's for — not a visibility change.
LEARN JAVA + ROBOT PROGRAMMING · B-LINE AUTOS
8
Notes: driveRobotRelative seems to do nothing: applyChassisSpeeds already exists and already does exactly this. But it's private — deliberately, since Lesson 10 — so that nothing outside Drivetrain could command the wheels without going through a command factory. A door punched in that wall on purpose, for one specific outside caller, is a normal and healthy thing to do; quietly making applyChassisSpeeds public would not be. Why isn't it a Command like everything else? Because B-Line is building the command. It needs a plain method it can call every tick from inside its own command. You write the method; the library decides when to call it.

## Slide 9
SECTION 4 · MEET PIDCONTROLLER
The class behind code you've written three times
Nothing to add — Lessons 5, 8 and 11, by hand
double error = target - measured;
double output = kP * error;
Nothing to add — this is just how the class is used
PIDController controller = new PIDController(5.0, 0.0, 0.0);
double output = controller.calculate(measured, target);
calculate(measured, target) is your two lines. The three numbers are the P, I and D gains — leave I and D at zero. What the class adds is state: it remembers past errors and knows a tolerance.
LEARN JAVA + ROBOT PROGRAMMING · B-LINE AUTOS
9
Notes: Lesson 5 steered a module with those two lines. Lesson 8 turned to a heading. Lesson 11 drove to a pose. WPILib has had a class for this the whole time, and now you need three of them at once, so it's finally worth reaching for. A plain P loop is genuinely the right answer for path following, and I and D are a different lesson's problem. Beyond tidiness, the class remembers the previous error so it can compute a derivative, accumulates error so it can integrate, and can be told a tolerance and asked whether it's there yet. B-Line uses all of that inside its follower — you just hand it the controllers.

## Slide 10
SECTION 4 · WHY THREE?
Chasing a line is three separate jobs
Translation
How much path is left? Error: meters remaining. Output: meters per second.
Rotation
Which way to face, independent of where you go. Error: radians. Output: rad/s.
Cross-track
Half a meter left of the line? Push sideways back onto it. Meters off → m/s.
Every gain is output per unit of error, per second — 1/s — so all three sit in the same ballpark.
LEARN JAVA + ROBOT PROGRAMMING · B-LINE AUTOS
10
Notes: The three loops pull in different directions. Translation drives faster when there's a lot of path left and eases off as you arrive. Rotation spins the chassis toward the heading the path asked for, with no regard for the driving — because swerve. Cross-track catches what neither of the others notices: you're headed the right way at the right speed, but you're half a meter to the left of the line. That's why the numbers are all in the same ballpark despite measuring different things.

## Slide 11
SECTION 4 · CONSTANTS.JAVA
Three gains, one new class
Add to Constants.java, as a new nested class after VisionConstants
public static final class PathConstants {
// BLine runs three P loops at once. Every gain here is "output per unit of
// error", and since error is meters (or radians) and output is per-second,
// the units all come out to 1/s.
public static final double kTranslationP = 5.0; // m/s per meter of path left
public static final double kRotationP = 3.0; // rad/s per radian of heading error
public static final double kCrossTrackP = 2.0; // m/s per meter off the line
}
Gains stay bare doubles, same as kDriveKV and HeadingConstants.kP — they're ratios, not physical quantities, so there's no unit for Units to carry.
LEARN JAVA + ROBOT PROGRAMMING · B-LINE AUTOS
11
Notes: kTranslationP is meters per second of speed for every meter of path left; kRotationP is radians per second for every radian of heading error; kCrossTrackP is meters per second of sideways push for every meter off the line. Section 5 comes back to kTranslationP, because it's half of the arithmetic that decides whether the robot can stop where you asked.

## Slide 12
SECTION 5 · DRAW A PATH
Three things you can place on the field
Waypoint
A position and a heading: "be here, facing this way."
TranslationTarget
A position only: "drive through this point, any heading."
RotationTarget
A heading only, partway along a segment: "by about here, face this way."
The split exists because swerve decouples the two: a robot can loop around an obstacle while slowly turning to face a target the whole time.
LEARN JAVA + ROBOT PROGRAMMING · B-LINE AUTOS
12
Notes: BLine Web is a path editor that runs in your browser: drop points on a picture of the field, drag them around, and export a .json file. The 2027 build you installed has its own beta editor, which BLine's 2027 guide lists at web-beta.bline-web.pages.dev — use that one, not the 2026 editor. Whether you draw it or type it, the result is a JSON file, and you should see one so the editor stops being magic. You want to say "where" and "which way" separately instead of pretending each corner needs a heading.

## Slide 13
SECTION 5 · NEW FILES
Paths live in the deploy folder
1
Right-click src/main/deploy → New Folder: autos
The deploy folder you've had since Lesson 0 — for files the robot reads.
2
Right-click autos → New Folder: paths
One JSON file per path goes in here.
3
Right-click paths → New File: TwoCorners.json, then FarSide.json
The next slides show what goes in each.
4
Right-click autos → New File: config.json
Speed limits shared by every path. Not optional.
LEARN JAVA + ROBOT PROGRAMMING · B-LINE AUTOS
13
Notes: Anything under src/main/deploy/ gets copied onto the robot next to your program when you deploy — it's for the files your code needs to read rather than compile. Paths are exactly that kind of file: you want to redraw one between matches without recompiling anything. The simulator reads from the same folder, so a path you drop in works in sim immediately.

## Slide 14
SECTION 5 · TWOCORNERS.JSON
Start at (3, 3), through (6, 3), turning toward 90°
Create src/main/deploy/autos/paths/TwoCorners.json — part 1
{
"path_elements": [
{
"type": "waypoint",
"translation_target": { "x_meters": 3.0, "y_meters": 3.0 },
"rotation_target": { "rotation_radians": 0.0 }
},
{
"type": "translation",
"x_meters": 6.0,
"y_meters": 3.0
},
{
"type": "rotation",
"rotation_radians": 1.5707963,
"t_ratio": 0.5,
"profiled_rotation": true
},
LEARN JAVA + ROBOT PROGRAMMING · B-LINE AUTOS
14
Notes: The simulated robot starts at (3, 3) facing 0° — that's DriveConstants.kSimStartingPose from Lesson 16 — so this path starts there too. A t_ratio of 0.5 is "halfway along this segment": rotations get placed by fraction-of-segment rather than by coordinate, since they don't have a position of their own. The simulated field is empty — Lesson 16's chassis has no walls and nothing to bump into — so a path can cross places a real robot couldn't. When you draw paths for a real field, draw them around its structures.

## Slide 15
SECTION 5 · TWOCORNERS.JSON
An event marker, then the end at (6, 6)
TwoCorners.json — part 2, finishing the file
{
"type": "event_trigger",
"t_ratio": 0.8,
"lib_key": "shoot"
},
{
"type": "waypoint",
"translation_target": { "x_meters": 6.0, "y_meters": 6.0 },
"rotation_target": { "rotation_radians": 3.1415927, "profiled_rotation": true }
}
]
}
Read it as a sentence: start at (3, 3) facing 0°, drive through (6, 3), face 90° halfway up the next leg, end at (6, 6) facing 180°.
LEARN JAVA + ROBOT PROGRAMMING · B-LINE AUTOS
15
Notes: The event_trigger element is for section 9 — leave it in for now. Angles here are radians, not degrees: 1.5707963 is 90° and 3.1415927 is 180°. The editor writes them for you; this is mostly a warning for when you hand-edit and wonder why 90 sent the robot somewhere strange.

## Slide 16
SECTION 5 · READING THE FILE
Two details that change what the robot does
"profiled_rotation": true turns the robot gradually
The heading the path asks for turns in step with progress along the path. Leave it out and the robot faces 90° before it even reaches the first corner.
Angles are radians, and t_ratio is a fraction
1.5707963 is 90°. A t_ratio of 0.5 means halfway along the segment the element sits in.
LEARN JAVA + ROBOT PROGRAMMING · B-LINE AUTOS
16
Notes: "profiled_rotation": true is what makes "by halfway up the next leg" true. With it, the heading the path asks for turns gradually, in step with how far along the path you are. Leave it out and the robot turns to face the next heading as fast as it can, the moment that target becomes the next one — on this path, that means it's already facing 90° before it reaches the first corner.

## Slide 17
SECTION 5 · CONFIG.JSON
How fast every path is allowed to go
Create src/main/deploy/autos/config.json
{
"kinematic_constraints": {
"default_max_velocity_meters_per_sec": 2.0,
"default_max_acceleration_meters_per_sec2": 6.0,
"default_max_velocity_deg_per_sec": 360.0,
"default_max_acceleration_deg_per_sec2": 720.0,
"default_end_translation_tolerance_meters": 0.05,
"default_end_rotation_tolerance_deg": 2.0,
"default_intermediate_handoff_radius_meters": 0.5
}
}
Handoff radius 0.5: start turning up the next leg half a meter before the corner, instead of driving all the way in.
LEARN JAVA + ROBOT PROGRAMMING · B-LINE AUTOS
17
Notes: config.json is not optional. B-Line reads it every time it loads a path, so a missing file is an error the moment the path loads, not a quiet default. The last number, handoff radius, is the cornering knob: how close the robot has to get to a point before it gives up on it and starts driving to the next one. The first two numbers deserve more than a glance, because they're not taste — that's the next slide.

## Slide 18
SECTION 5 · NOT TASTE — PHYSICS
Can it stop in time? Two lines of arithmetic
AT 2 m/s — THE SHIPPED LIMIT
0.40 m
warning: 2.0 ÷ 5.0
0.33 m
to stop: 2² ÷ (2 × 6)
Fits — the robot arrives
AT 3 m/s
0.60 m
warning: 3.0 ÷ 5.0
0.75 m
to stop: 3² ÷ (2 × 6)
Doesn't fit — it sails past
B-Line plans nothing ahead: acceleration alone decides if it can stop.
LEARN JAVA + ROBOT PROGRAMMING · B-LINE AUTOS
18
Notes: The translation loop just asks for kTranslationP × distance left, capped at the max speed, and the acceleration limit decides how fast the robot is allowed to change what it's doing. The loop starts slowing the robot when 5.0 × distance left drops below the top speed — at 2 m/s, that's 0.4 m from the end. Stopping from 2 m/s at 6 m/s² takes 0.33 m. 0.33 m of stopping fits inside 0.4 m of warning, so the robot arrives. At 3 m/s it wouldn't. The same limit governs corners — turning 2 m/s of "east" into 2 m/s of "north" is a change in velocity like any other — and with these numbers the robot swings roughly 5–12 cm past the first corner. If one thing from this lesson sticks, make it this: you can do this math before the robot ever moves.

## Slide 19
SECTION 5 · FARSIDE.JSON
A second path, from the same start
Create src/main/deploy/autos/paths/FarSide.json
{
"path_elements": [
{
"type": "waypoint",
"translation_target": { "x_meters": 3.0, "y_meters": 3.0 },
"rotation_target": { "rotation_radians": 0.0 }
},
{
"type": "translation",
"x_meters": 9.0,
"y_meters": 3.0
},
{
"type": "waypoint",
"translation_target": { "x_meters": 9.0, "y_meters": 1.0 },
"rotation_target": { "rotation_radians": -1.5707963, "profiled_rotation": true }
}
]
}
LEARN JAVA + ROBOT PROGRAMMING · B-LINE AUTOS
19
Notes: Real robots carry several autos, and having two here makes something visible in section 7 that one path would hide. It starts at the same place as Two Corners, then runs past the middle of the field and turns right, ending up facing −90°.

## Slide 20
SECTION 6 · AUTOS.JAVA
FollowPath.Builder: everything about this robot
Add to Autos, below driveTurnDrive
/** Everything about following a path that doesn't depend on which path it is. */
public static FollowPath.Builder makePathBuilder(Drivetrain drivetrain, Localizer localizer) {
return new FollowPath.Builder(
DriveType.SWERVE, // what kind of drivetrain this is
drivetrain, // the mechanism the command will require
localizer::getPose, // where we are (fused, Lesson 14)
localizer::resetPose, // how to tell the estimate where we are
drivetrain::getChassisVelocities, // how fast we're going, robot-relative
drivetrain::driveRobotRelative, // how to make the robot move
new PIDController(PathConstants.kTranslationP, 0, 0),
new PIDController(PathConstants.kRotationP, 0, 0),
new PIDController(PathConstants.kCrossTrackP, 0, 0))
.withDefaultShouldFlip() // mirror the path for the red alliance
.withTelemetry(Telemetry.getTable()); // log what the follower is doing
}
LEARN JAVA + ROBOT PROGRAMMING · B-LINE AUTOS
20
Notes: B-Line needs a handful of facts about your specific robot before it can drive it down a line, and FollowPath.Builder is where you hand them over. Once it has them, build(path) turns a Path into an ordinary Commands V3 Command. Everything about following a path lives in Autos, next to driveTurnDrive, because it's all about autonomous — so that's where the builder gets made. Nine arguments, and you've already met every idea in them.

## Slide 21
SECTION 6 · AUTOS.JAVA
Imports, and the first two arguments
Add to Autos's imports
import org.wpilib.math.controller.PIDController;
import org.wpilib.telemetry.Telemetry;
import first.robot.Constants.PathConstants;
import first.robot.subsystems.Localizer;
import frc.robot.lib.BLine.commands.FollowPath;
import frc.robot.lib.BLine.following.DriveType;
DriveType.SWERVE, then the mechanism it requires
B-Line drives tank and mecanum too. The drivetrain argument is Lesson 9's mutual exclusion: teleop driving steps aside while a path runs.
LEARN JAVA + ROBOT PROGRAMMING · B-LINE AUTOS
21
Notes: The first argument says what kind of drivetrain this is — B-Line can drive tank and mecanum robots too, and it follows a path differently for each. The second is the mechanism the command requires — Lesson 9's mutual exclusion, so your teleop drive command steps aside while a path is running.

## Slide 22
SECTION 6 · METHOD REFERENCES
Two of them fetch a value; two of them are verbs
SUPPLIERS
localizer::getPose, drivetrain::getChassisVelocities
Fetch a value when asked — like the joystick suppliers back in Lesson 2.
VERBS
drivetrain::driveRobotRelative, localizer::resetPose
Return nothing. B-Line calls them — every tick with a motion, or once with a pose.
Then three separate PIDControllers: translation, rotation, cross-track.
LEARN JAVA + ROBOT PROGRAMMING · B-LINE AUTOS
22
Notes: The next four arguments are section 3's two new doors plus Lesson 14's pose and reset, all handed over as method references. drivetrain::driveRobotRelative doesn't return anything — B-Line calls it, every tick, with the chassis motion it has decided on. localizer::resetPose is the same shape: B-Line calls it with a pose. You're not handing over a value, or even a way to get one. You're handing over a verb. The three PIDControllers come in the order the builder expects them, and they have to be three separate objects — hand the builder the same controller twice and it throws an error the moment it's made.

## Slide 23
SECTION 6 · NOTICE WHAT'S MISSING
The path isn't in it — one builder serves every path
Two settings chained on the end
withDefaultShouldFlip() mirrors the path for the red alliance — draw once, works on both. withTelemetry(...) logs what B-Line is doing under FollowPath/.
Every argument describes this robot, not one line
So one builder can serve every path you'll ever draw. Sharing its controllers is safe: every command it makes requires the drivetrain.
LEARN JAVA + ROBOT PROGRAMMING · B-LINE AUTOS
23
Notes: That's why makePathBuilder takes only the drivetrain and the localizer, and why it hands back the builder instead of a finished command. One builder means one set of controllers for every auto, and that's safe: every command the builder makes requires the drivetrain, so the scheduler guarantees only one of them is ever running. And B-Line resets the controllers each time a path starts, so each run starts clean. The telemetry — cross-track error, distance left, which point it's heading for — is what section 10 plots.

## Slide 24
SECTION 6 · AUTOS.JAVA
Turning a path into something you can schedule
Add to Autos, below makePathBuilder
/** One drawn path, as a command. */
public static Command followPath(FollowPath.Builder pathBuilder, Path path) {
return pathBuilder.build(path)
.withPoseReset(); // start by telling the estimate we're at the path's start
}
Add to Autos's imports
import frc.robot.lib.BLine.path.Path;
withPoseReset(): "we're at the start of the path, trust me." True on a real field because a person put the robot there.
LEARN JAVA + ROBOT PROGRAMMING · B-LINE AUTOS
24
Notes: It takes a Path — a path file, already read in; section 7 is where that happens. withPoseReset() asks B-Line to call localizer::resetPose with the path's starting pose the moment the path starts. On a real field that's true because a person put the robot there, which is exactly why it's worth doing — the estimate starts the auto knowing where the robot is instead of guessing. Hold on to that "because a person put it there"; section 8 is about what happens when nobody did.

## Slide 25
SECTION 6 · ROBOT.JAVA
Built once, where the drivetrain lives
Add to Robot, below the camera fields
public final LimelightPoseProvider frontCamera;
public final LimelightPoseProvider backCamera;
// How this robot follows a path. It's the same for every path, so it's
// built once, here, and every autonomous opmode reaches in and uses it.
public final FollowPath.Builder pathBuilder = Autos.makePathBuilder(drivetrain, localizer);
Add to Robot's imports
import first.robot.commands.Autos;
import frc.robot.lib.BLine.commands.FollowPath;
Robot lives for the whole program; opmodes are rebuilt on every selection.
LEARN JAVA + ROBOT PROGRAMMING · B-LINE AUTOS
25
Notes: The builder needs a home that's built once and reachable from every autonomous opmode, and you already have exactly that place. It goes in Robot for the same reason the drivetrain does: opmodes are rebuilt every time they're selected, and Robot is the thing that lives for the whole program. It's a field initializer that uses drivetrain and localizer, so it has to come after both — it does, since they're declared above it.

## Slide 26
SECTION 7 · NEW FILES
One opmode per path
1
Right-click opmode → New File: RobotAutoTwoCorners.java
The next two slides show the whole file.
2
Right-click opmode → New File: RobotAutoFarSide.java
Same file, three words changed: the class name, "Far Side", "FarSide".
3
Both say group = "Paths"
A group of their own on the opmode selector, apart from Lesson 9's.
Why not one opmode with a menu inside it? Because the Driver Station already is the menu — each auto is one small file, no chooser code.
LEARN JAVA + ROBOT PROGRAMMING · B-LINE AUTOS
26
Notes: In Lesson 9 you learned how this framework offers a choice of autos: every @Autonomous class is its own entry on the Driver Station's opmode selector. A path auto is one more of those. The class name RobotAutoFarSide appears in both places — the class line and the constructor — and the path file's name is "FarSide". It's the same pattern Lesson 9 set up with Do Nothing.

## Slide 27
SECTION 7 · ROBOTAUTOTWOCORNERS.JAVA
The top of the file
Create opmode/RobotAutoTwoCorners.java — part 1
// Copyright (c) FIRST and other WPILib contributors.
// Open Source Software; you can modify and/or share it under the terms of
// the WPILib BSD license file in the root directory of this project.
package first.robot.opmode;
import org.wpilib.command3.button.RobotModeTriggers;
import org.wpilib.opmode.Autonomous;
import org.wpilib.opmode.PeriodicOpMode;
import first.robot.Robot;
import first.robot.commands.Autos;
import frc.robot.lib.BLine.path.Path;
@Autonomous(name = "Two Corners", group = "Paths")
public class RobotAutoTwoCorners extends PeriodicOpMode {
private final Robot robot;
LEARN JAVA + ROBOT PROGRAMMING · B-LINE AUTOS
27
Notes: name = "Two Corners" is what the opmode selector shows; group = "Paths" sorts it into its own group. The robot field holds the Robot that the framework hands every opmode's constructor, the same as Lesson 9's RobotAuto.

## Slide 28
SECTION 7 · ROBOTAUTOTWOCORNERS.JAVA
Read the file now; run it on enable
RobotAutoTwoCorners.java — part 2, finishing the class
public RobotAutoTwoCorners(Robot robot) {
this.robot = robot;
// Read the path file now, while the robot is still disabled.
Path path = new Path("TwoCorners");
// Runs on enable.
RobotModeTriggers.autonomous().onTrue(Autos.followPath(robot.pathBuilder, path));
}
@Override
public void periodic() {
/* Called periodically (set time interval) while the robot is enabled. */
}
}
LEARN JAVA + ROBOT PROGRAMMING · B-LINE AUTOS
28
Notes: new Path("TwoCorners") opens deploy/autos/paths/TwoCorners.json, reads it, and reads config.json alongside it — the .json is added for you. The autonomous trigger is the same one Lesson 9's RobotAuto uses: it schedules the path the moment autonomous is enabled.

## Slide 29
SECTION 7 · THE PART WORTH UNDERSTANDING
An opmode's constructor runs when it's selected
The path file is read while the robot sits disabled
Minutes before the match — so when autonomous starts, the command is already built and just has to run.
A mistake shows up in the pits, not on the field
Misspell "TwoCorner" and new Path(...) throws an IllegalArgumentException naming the missing file — the moment you select the auto.
LEARN JAVA + ROBOT PROGRAMMING · B-LINE AUTOS
29
Notes: An opmode's constructor runs the moment it's selected on the Driver Station — not when you enable. That's how Lesson 9's binding got scoped to its opmode, and it has a second consequence here: the new Path(...) line runs at selection time too. That matters more than it sounds. Reading and checking a file isn't free, and the start of autonomous is the one moment you can't afford to spend on setup.

## Slide 30
SECTION 8 · PUT THE ROBOT WHERE THE PATH STARTS
withPoseReset() makes a promise on your behalf
On a real field, a person keeps it
Someone carries the robot out and sets it down at the start. In the simulator, nobody does.
Broken twice in the simulator
Run an auto a second time: the robot is where the last run ended. Or first time: SimGUI starts on Red 1, so the path flips while the robot sits at the blue start.
LEARN JAVA + ROBOT PROGRAMMING · B-LINE AUTOS
30
Notes: Break that promise and the robot gets told a pose it isn't at. The cameras still see where it really is, so within about a second they drag the estimate's position back to the truth. They don't fix its heading, so the robot goes on believing it faces the wrong way and drives off in strange directions. SimGUI's DS window says Red 1, and the first time you click Autonomous it tells the robot so. withDefaultShouldFlip() from section 6 does exactly its job — it mirrors the path to the red end of the field and resets the estimate there — while the simulated robot is still sitting at the blue start, most of a field away. So do the person's job in the simulator: when an auto is selected, set the simulated robot down where that auto starts. Three small pieces.

## Slide 31
SECTION 8 · CHASSISSIMULATION.JAVA
Piece 1: set the chassis down, at rest
Add to ChassisSimulation, above getPose
/** Set the chassis down at 'pose', at rest — what a person does before a match. */
public void placeAt(Pose2d pose) {
m_pose = pose;
m_velocity = new ChassisVelocities();
}
"At rest" is the second line: a robot you've just set down isn't moving, so whatever velocity the chassis was carrying goes too.
LEARN JAVA + ROBOT PROGRAMMING · B-LINE AUTOS
31
Notes: ChassisSimulation is Lesson 16's ground truth — the one place that knows where the simulated chassis really is. Setting it down means replacing its pose and zeroing its velocity.

## Slide 32
SECTION 8 · DRIVETRAIN.JAVA
Piece 2: a sim-only door that does nothing for real
Add to Drivetrain, below getSimulatedPose
/**
* Sim only: set the simulated chassis down at 'pose', the job a person does
* before a real match. Does nothing on a real robot.
*/
public void placeSimulatedRobot(Pose2d pose) {
if (m_chassisSim != null) {
m_chassisSim.placeAt(pose);
}
}
The same null check as simulateChassis: a real robot has no m_chassisSim. The gyro turns with it — Lesson 16's GyroIOSim reads its heading off the chassis.
LEARN JAVA + ROBOT PROGRAMMING · B-LINE AUTOS
32
Notes: On a real robot there's no m_chassisSim, because a person does this job. Nothing else needs telling, either: Lesson 16's GyroIOSim reads its heading straight off the simulated chassis, so the gyro turns with it.

## Slide 33
SECTION 8 · AUTOS.JAVA
Piece 3: where does this auto start, on our side?
Add to Autos, below followPath
/** Where a path starts, on this alliance's side of the field — the same flip BLine makes. */
public static Pose2d startPose(Path path) {
Pose2d start = path.getAuthoredStartPose().get(); // every path here starts with a waypoint
boolean red = MatchState.getAlliance().orElse(Alliance.BLUE) == Alliance.RED;
return red ? FlippingUtil.flipFieldPose(start) : start;
}
Add to Autos's imports
import org.wpilib.driverstation.Alliance;
import org.wpilib.driverstation.MatchState;
import org.wpilib.math.geometry.Pose2d;
import frc.robot.lib.BLine.field.FlippingUtil;
LEARN JAVA + ROBOT PROGRAMMING · B-LINE AUTOS
33
Notes: The third piece answers "where does this auto start?", on whichever side of the field the robot is playing. FlippingUtil.flipFieldPose comes from B-Line itself, so the robot is set down exactly where the flipped path starts.

## Slide 34
SECTION 8 · READING STARTPOSE
Two Optionals, and the mirror B-Line uses
getAuthoredStartPose().get()
A path could begin with a bare rotation and have no start of its own. Yours begin with a waypoint, so .get() is safe — and crashes loudly if not.
getAlliance().orElse(Alliance.BLUE)
Until the Driver Station says, there is no alliance. orElse takes what's in the box, or blue if it's empty — the rule B-Line's flip follows.
LEARN JAVA + ROBOT PROGRAMMING · B-LINE AUTOS
34
Notes: Both are Lesson 15's Optional — a box that might be empty. getAuthoredStartPose() is one because a path could begin with a bare rotation and have no starting spot of its own; if you ever draw one like that, .get() crashes right there, which is what you'd want. MatchState.getAlliance() is the other: until the Driver Station says, there is no alliance. Then FlippingUtil.flipFieldPose mirrors the pose the same way B-Line mirrors the path.

## Slide 35
SECTION 8 · BOTH AUTO OPMODES
Set the robot down when the auto is selected
Add the placement to both auto opmodes' constructors, between the two lines you have
public RobotAutoTwoCorners(Robot robot) {
this.robot = robot;
// Read the path file now, while the robot is still disabled.
Path path = new Path("TwoCorners");
// In the simulator, set the robot down at the path's start — the job a
// person does on a real field. On a real robot this does nothing.
robot.drivetrain.placeSimulatedRobot(Autos.startPose(path));
// Runs on enable.
RobotModeTriggers.autonomous().onTrue(Autos.followPath(robot.pathBuilder, path));
}
Selected: set down. Disabled after a run: rebuilt, and set down again.
LEARN JAVA + ROBOT PROGRAMMING · B-LINE AUTOS
35
Notes: The constructor is exactly the right moment, for the same reason it's the right moment to read the file: it runs when the auto is selected, while the robot is disabled — when, on a real field, someone is setting the robot down. And it runs again every time you disable after an auto has run, because the framework rebuilds the opmode then. So every run starts from the start, on whichever side of the field you're playing. Make the same change in RobotAutoFarSide.

## Slide 36
SECTION 9 · EVENT MARKERS
A named point on the path that fires an action
Add to Autos, below startPose
/** Names a path file can fire with lib_key. BLine keeps them for the whole program. */
public static void registerEventTriggers() {
// Nothing on this robot can shoot yet, so it just says so in the console.
FollowPath.registerEventTrigger("shoot", () -> System.out.println("Event: shoot!"));
}
Add to Robot's constructor, after the addEventListener line
public Robot() {
DataLogManager.start(); // saves every published value to a .wpilog file
Scheduler.getDefault().addEventListener(this::logCommandStart);
Autos.registerEventTriggers(); // once, for the whole program
// ...
}
LEARN JAVA + ROBOT PROGRAMMING · B-LINE AUTOS
36
Notes: Real autos do things along the way — spin up a shooter while still driving, drop an intake before arriving. The name is the link: a path file refers to a marker by lib_key, and your code registers what that key should do. Registration is static — B-Line keeps one table for the whole program, not one per path — so it happens once, and once for the whole program means the constructor of the thing that lives for the whole program. The second argument is a lambda that takes nothing and returns nothing — a plain action, which Java calls a Runnable. B-Line runs it once, on the loop after the robot passes the marker. It has to be quick: it runs inside the robot's loop. registerEventTrigger also accepts a Command, for an event that needs to keep running for a while.

## Slide 37
SECTION 9 · THE PATH SIDE
Already in your file since section 5
Nothing to add — this is already in TwoCorners.json
{
"type": "event_trigger",
"t_ratio": 0.8,
"lib_key": "shoot"
},
80% along its own segment
The second leg, from (6, 3) to (6, 6) — the same fraction idea rotations use.
A misspelled key won't crash
B-Line logs "Unregistered event trigger key: Shoot" and keeps driving. Check the console first.
LEARN JAVA + ROBOT PROGRAMMING · B-LINE AUTOS
37
Notes: B-Line looks the name up when the robot reaches the marker, not when the path loads, and an unknown key just logs "FollowPath: Unregistered event trigger key: Shoot" and keeps driving. So if a marker never seems to fire, check the console for that line before you go hunting in the geometry.

## Slide 38
SECTION 10 · RUN IT
Blue 1 first, then pick the auto and enable
1
./gradlew simulateJava → DS window: Alliance Station = Blue 1
Editable only while Disconnected. SimGUI starts on Red 1 every time.
2
Click Autonomous, pick Two Corners
Console: Creating OpMode Two Corners — path read, robot set down.
3
Set state to Enabled
About 4 s: out along X, up the second leg, settling at (6, 6).
4
To run again: Disabled, then Enabled
The opmode is rebuilt and the robot set back down at (3, 3).
LEARN JAVA + ROBOT PROGRAMMING · B-LINE AUTOS
38
Notes: Red works too now — that's Try It #6 — but the numbers in this walkthrough are for blue. Pick Far Side and the Creating OpMode line prints again for that one; pick Two Corners back before you enable. The robot finishes within the tolerances in config.json — within 5 cm and 2° — so don't be surprised to read 178.3° rather than 180°. If you want to watch section 8's problem happen, comment out the placeSimulatedRobot line and run twice without restarting.

## Slide 39
SECTION 10 · WHAT TO WATCH
The line, the belief, and the truth
1
Odometry tab: Localizer/Pose
An actual shape — the corner rounded, 90° partway up, 180° at the end.
2
Add Drivetrain/SimulatedPose
Where the robot thinks it is and where it is, within a couple of cm.
3
Plot FollowPath/crossTrackError
Jumps to about 0.5 m at the corner — the handoff radius — then shrinks.
Nothing told the follower it was off the line. Correcting is the only thing it ever does.
LEARN JAVA + ROBOT PROGRAMMING · B-LINE AUTOS
39
Notes: Watch it the way you've watched every closed-loop lesson since Lesson 5 — asked-for against measured. Event: shoot! shows up in the console about 80% of the way up the second leg. FollowPath/crossTrackError is the cross-track loop's error and FollowPath/remainingPathDistanceMeters is the translation loop's. The cross-track error jumps right at the corner because the robot is still on the first leg's line when it starts measuring against the second's, then shrinks back toward zero as the cross-track loop pulls the robot onto the second leg.

## Slide 40
BEFORE YOU MOVE ON
Try it
1
Add a third path
WRITE CODE
One JSON file and one opmode. Building a second Builder? Re-read section 6.
2
Break the math
WRITE CODE
Handoff 0.05: tighter or wider corner? Predict, run. Then try 3 m/s.
3
Mistune a gain
WRITE CODE
kCrossTrackP 0.0 swings wide; 15.0 oscillates and never finishes.
4
Path, then script
WRITE CODE
Follow TwoCorners, then turnToHeading(0): two coroutine.await calls.
LEARN JAVA + ROBOT PROGRAMMING · B-LINE AUTOS
40
Notes: 1: It should be one new JSON file and one new opmode whose constructor is Two Corners' three lines with a different file name. Your path can start anywhere — the robot is set down wherever it begins. 2: In this course's sim, a 0.05 handoff swings the robot about half a meter past the first corner instead of 5–12 cm, and takes half a second longer — a later handoff means it drives into the corner at full speed before it starts turning. At 3 m/s, section 5's arithmetic says it can't stop in time: it sails roughly 30 cm past the end and about 60 cm past the first corner. Then change the acceleration so the arithmetic works again. 3: With kCrossTrackP at 0.0 the robot swings about half a meter wide at the corner, because nothing pulls it back onto the second leg. At 15.0 it swings back and forth across the line near the end — about a third of a meter each way — and is still swinging 30 seconds later. Plot FollowPath/crossTrackError for both. 4: A library-built command and one you wrote are both just Commands, so Lesson 9's Command.noRequirements(coroutine -> { ... }) with two coroutine.await(...) calls is all it takes.

## Slide 41
BEFORE YOU MOVE ON
Try it, continued
5
A real marker job
WRITE CODE
Swap the println for Telemetry.log("Auto/ShootFired", true). Check it fires where you placed it, then move the t_ratio and watch the timing move.
6
Run it on red
Disconnected, Alliance Station Red 1, Autonomous, Two Corners. The robot is set down at (13.54, 5.07) and runs the mirrored path. Predict: what if startPose didn't flip?
LEARN JAVA + ROBOT PROGRAMMING · B-LINE AUTOS
41
Notes: 5 is a real code edit in registerEventTriggers; confirm on the plot that the value flips where you placed the marker. 6 needs no code: the robot is set down at the red end, (13.54, 5.07) facing 180°, and runs the same shape rotated half a turn, finishing near (10.54, 2.07) facing 0°. Nothing in your code changed — withDefaultShouldFlip() and startPose agree about which side of the field you're on. If startPose didn't flip, you'd be back to section 8's problem: a flipped path, and a robot set down at the blue start.

## Slide 42
WHAT YOU LEARNED
Autonomous stopped being a script
A path is a shape in a file, and the follower's only job is to chase it — so drifting off the line no longer ruins the auto.
Three PIDControllers, three separate jobs: distance-to-go, heading, and drift off the line.
Speed limits are arithmetic: where slowing starts, and how far stopping takes.
Notice when code runs: the opmode's constructor reads the path, and sets the sim robot down, at selection.
NEXT
Lesson 18
Scoring Elevator
Holding a position, not just reaching one.
LEARN JAVA + ROBOT PROGRAMMING · B-LINE AUTOS
42
Notes: That switch is only possible because of what Lesson 14 built: chasing a line requires knowing where you are, continuously and honestly. Two habits outlive B-Line entirely. Build the unchanging thing once — one FollowPath.Builder in Robot serves every path. And notice when your code runs, not just what it does. withPoseReset() is a promise about the world — "a person put the robot here" — and in the simulator you had to keep it yourself, at the same moment a person would. The drivetrain half of this course is done. Your robot drives itself along drawn paths, knows where it is from three kinds of evidence, and lives in a simulated world with real limits on grip. What it doesn't have is anything to do when it arrives. That's next.