## Slide 1
LEARN JAVA + ROBOT PROGRAMMING
LESSON 10
Full Swerve with Kinematics
Translate and rotate at the same time
WPILib 2027 Alpha · Commands V3
Notes: Lesson 7's translate handles "drive in a direction." Lesson 8's rotate handles "spin in place." What neither one does is both at once — this lesson replaces both with SwerveDriveKinematics so the chassis can translate and rotate at the same time, the "full swerve" behavior every real swerve robot needs.

## Slide 2
THE GOAL
One drive command that mixes translation and spin
Replace the hand-rolled translate and rotate with SwerveDriveKinematics — full swerve, plus always steering the shortest path.
NEW JAVA CONCEPTS
Immutable data-carrier objects
Indexed for loops, for pairing two arrays
MathUtil.inputModulus — the wrap loop, graduated
Scaling a typed measure by a fraction
NEW ROBOT CONCEPTS
SwerveDriveKinematics
ChassisVelocities and SwerveModuleVelocity
Speed desaturation and state optimization
Field-relative driving, using the gyro
LEARN JAVA + ROBOT PROGRAMMING · FULL SWERVE
2
Notes: Give SwerveDriveKinematics a ChassisVelocities; it hands back four SwerveModuleVelocitys — the same type you've been logging to the Swerve tab since Lesson 7. Today that type stops being just telemetry and becomes the language the whole drivetrain speaks.

## Slide 3
SECTION 1 · WHY KINEMATICS?
Neither command does both at once
translate and rotate both require the Drivetrain.
So scheduling one cancels the other. Real swerve robots drive and spin constantly — sweeping around a defender while a shooter stays pointed at the goal. At each corner, add the translation velocity vector to the rotation velocity vector, and you get motion that does both.
SwerveDriveKinematics packages that math so you never re-derive it: give it a ChassisVelocities, it hands back four SwerveModuleVelocitys.
LEARN JAVA + ROBOT PROGRAMMING · FULL SWERVE
3
Notes: Each calls setDesiredState on every module, and since translate and rotate both require the Drivetrain, scheduling one cancels the other — that's the actual mechanical reason neither can run alongside the other, not just a design choice. The math is simple once spelled out: at each corner, add the translation velocity vector to the rotation velocity vector (which points tangent to the circle around the center, with magnitude ω × r). WPILib packages it as SwerveDriveKinematics so you never have to re-derive it.

## Slide 4
SECTION 2 · DRIVETRAIN.JAVA & CONSTANTS.JAVA
Built from the modules' locations
Add to Drivetrain, directly below the m_modules field
private final SwerveDriveKinematics m_kinematics = new SwerveDriveKinematics(
m_modules[0].location, m_modules[1].location,
m_modules[2].location, m_modules[3].location); // FL, FR, BL, BR
Add to DriveConstants
public static final LinearVelocity kMaxSpeed =
MetersPerSecond.of(100.0 / kDriveGearRatio * kWheelCircumferenceMeters); // ≈4.7 m/s
public static final AngularVelocity kMaxAngularSpeed = RotationsPerSecond.of(1.0);
LEARN JAVA + ROBOT PROGRAMMING · FULL SWERVE
4
Notes: The order the corners are listed in matters — whatever order you list them here is the order toSwerveModuleVelocities returns states in. Match the array built in Lesson 7 (FL, FR, BL, BR) exactly; a swapped pair produces a robot that almost drives right, which is the most confusing kind of wrong. What's new today is that WPILib's own kinematics types speak Units too: ChassisVelocities, SwerveModuleVelocity, and SwerveDriveKinematics all take measures directly, so a LinearVelocity flows straight through them — you don't unpack it to a double until you hit something that genuinely only speaks numbers, like Phoenix's setThrottle. MetersPerSecond.of(...) builds a LinearVelocity from a plain number — the arithmetic stays in doubles (readable), and the result becomes unit-aware. That's the pattern for making one: compute in doubles, wrap the answer. Worth naming: this is close to the "5" eyeballed for the Swerve tab's Max Speed back in Lesson 7 — now it's a computed, typed constant instead of a guess.

## Slide 5
SECTION 3 · SWERVEMODULE.JAVA
One state in, chase it
Replace the two-argument setDesiredState with
/** One tick of control: chase the given state. */
public void setDesiredState(SwerveModuleVelocity state) {
double error = MathUtil.inputModulus(
state.angle.getDegrees() - getSteerAngleDegrees(), -180, 180);
double steerOutput = clamp(SteerConstants.kP * error, -1.0, 1.0);
m_steerMotor.setThrottle(steerOutput);
double alignment = Math.cos(Math.toRadians(error));
double fraction = state.velocity / DriveConstants.kMaxSpeed.in(MetersPerSecond);
m_driveMotor.setThrottle(fraction * alignment);
}
The two while loops from Lesson 5 collapse into MathUtil.inputModulus(value, -180, 180) — the one-liner, now that you've built the hand-rolled version and know what it does.
LEARN JAVA + ROBOT PROGRAMMING · FULL SWERVE
5
Notes: Your clamp two lines down doesn't get the same MathUtil treatment — this alpha's MathUtil has no clamp to graduate to, so the private helper from Lesson 5 stays, permanently, same as it did in Lesson 7. kMaxSpeed.in(MetersPerSecond) is the Units boundary in action: the constant is a typed LinearVelocity, but the division needs a plain number, so .in(...) hands one back. Worth noting explicitly: state.velocity is read as a plain double, not unpacked with .in(...) — SwerveModuleVelocity's constructor accepts a LinearVelocity if you want to build one that way, but the value it actually stores is a bare double in meters per second. Units at the boundary where you build the value, plain numbers once it's inside a kinematics type built for speed — you'll see the same thing on ChassisVelocities in a moment. Also worth a callout: this alpha ships SwerveModuleVelocity.cosineScale(Rotation2d) doing exactly the alignment trick here, built in — it's not used because the hand-rolled version already lives right next to the P control it depends on, and moving it wouldn't simplify anything.

## Slide 6
SECTION 3 CONTINUED · DRIVETRAIN.JAVA
Fix the caller the compiler already knows about
Update driveDistance from Lesson 9 — the old two-argument setDesiredState(0.0, 0.4) no longer compiles
// while driving forward:
module.setDesiredState(new SwerveModuleVelocity(
DriveConstants.kMaxSpeed.times(0.4), Rotation2d.fromDegrees(0)));
// to stop — after the loop, AND again inside whenCanceled:
module.setDesiredState(new SwerveModuleVelocity());
Same fix anywhere else you called the two-argument setDesiredState — let the compiler's red list walk you to each one, Lesson 7 style. .times(0.4) scales the max-speed measure and stays a LinearVelocity; new SwerveModuleVelocity() with no arguments means zero speed.
LEARN JAVA + ROBOT PROGRAMMING · FULL SWERVE
6
Notes: Lesson 9's driveDistance called setDesiredState(0.0, 0.4) to drive and setDesiredState(0.0, 0.0) twice to stop (once after the loop finishes on its own, once inside whenCanceled for an interruption) — none of that compiles anymore. Build a state instead: new SwerveModuleVelocity(DriveConstants.kMaxSpeed.times(0.4), Rotation2d.fromDegrees(0)) to drive, and new SwerveModuleVelocity() — zero speed — everywhere it used to stop. This is deliberately compiler-driven, the same habit Lesson 7 taught: change the signature, let the red squiggly list walk you to every call site rather than trying to remember them all.

## Slide 7
SECTION 4 · DRIVETRAIN.JAVA
Publish the desired states too
Add to Drivetrain, alongside m_moduleStatesPublisher
private final StructArrayPublisher<SwerveModuleVelocity> m_desiredModuleStatesPublisher =
NetworkTableInstance.getDefault()
.getStructArrayTopic("Drivetrain/DesiredModuleStates", SwerveModuleVelocity.struct)
.publish();
The helper you're about to write publishes into this.
applyChassisSpeeds is about to publish the chassis's desired states right next to Lesson 7's measured ones. Same StructArrayPublisher shape as m_moduleStatesPublisher, just a new topic name and a field to hold it.
LEARN JAVA + ROBOT PROGRAMMING · FULL SWERVE
7
Notes: The helper about to get built is going to publish the chassis's desired states right next to Lesson 7's measured ones, so it needs a second publisher first — same shape as m_moduleStatesPublisher, new topic name Drivetrain/DesiredModuleStates. Section 6 is where this pair of publishers pays off: dropping both ModuleStates and DesiredModuleStates into the Swerve tab's States slots shows two sets of arrows, where the wheels are told to be versus where they actually are.

## Slide 8
SECTION 4 · DRIVETRAIN.JAVA
Convert, desaturate, optimize, command
Add to Drivetrain
/** One tick of chassis motion: convert, desaturate, optimize, command. */
private void applyChassisSpeeds(ChassisVelocities speeds) {
SwerveModuleVelocity[] states = m_kinematics.toSwerveModuleVelocities(speeds);
// Scale ALL wheels down together if any one would exceed the max.
states = SwerveDriveKinematics.desaturateWheelVelocities(states, DriveConstants.kMaxSpeed);
m_lastCommandedOmega = speeds.omega / (2 * Math.PI); // rev/s for sim
for (int i = 0; i < m_modules.length; i++) {
states[i] = states[i].optimize(
Rotation2d.fromDegrees(m_modules[i].getSteerAngleDegrees()));
m_modules[i].setDesiredState(states[i]);
}
m_desiredModuleStatesPublisher.set(states);
}
LEARN JAVA + ROBOT PROGRAMMING · FULL SWERVE
8
Notes: This is Lesson 8's own trick again: every path into the drivetrain — stick driving, heading turns, and a future lesson's pose chasing — ends with the same four steps, so those four steps become one private helper and everything else becomes a thin caller. new ChassisVelocities(vx, vy, ω) packs "what I want the whole robot to do" into a single value; toSwerveModuleVelocities is the library math this lesson exists for, one chassis motion in, one SwerveModuleVelocity[] out, one entry per corner in the order given to the constructor. desaturateWheelVelocities matters at the edge of the envelope: if translation-plus-rotation asks one wheel for 6 m/s but the max is 4.7, it scales all four down so the motion keeps its shape, just slower — without it, the overasked wheel silently caps and the robot curves off course. Now the real trap: optimize doesn't change states[i] in place — it's a pure function, same as Rotation2d.rotateBy or Translation2d.plus — it returns a new SwerveModuleVelocity, and the original is untouched. Call states[i].optimize(...) and throw away the result, and nothing happens — the module gets commanded with the un-optimized state, silently. That's why the loop reads states[i] = states[i].optimize(...) — assign it back before it's used. The indexed for loop is the new shape here because states[i] has to be paired with m_modules[i], and pairing two arrays takes an index. m_lastCommandedOmega keeps Lesson 8's fake gyro fed, and m_desiredModuleStatesPublisher.set(states) publishes the desired states right next to Lesson 7's measured ones — the pair built on the previous slide.

## Slide 9
SECTION 4 · DRIVETRAIN.JAVA
Every path funnels through one helper
Add to Drivetrain
public Command drive(
Supplier<LinearVelocity> vx, Supplier<LinearVelocity> vy, Supplier<AngularVelocity> omega) {
return runRepeatedly(() -> applyChassisSpeeds(
new ChassisVelocities(vx.get(), vy.get(), omega.get()))).named("Drive");
}
Replace commandRotation in Drivetrain
private void commandRotation(double omegaRevPerSec) {
applyChassisSpeeds(new ChassisVelocities(0, 0, omegaRevPerSec * 2 * Math.PI));
}
delete translate and rotate — kinematics subsumes both. turnToHeading keeps working without a single edit, because commandRotation still exists underneath it.
LEARN JAVA + ROBOT PROGRAMMING · FULL SWERVE
9
Notes: Delete the translate and rotate command factories from Drivetrain — kinematics subsumes both. But don't delete commandRotation: Lesson 8's turnToHeading still calls it, and breaking a working command isn't part of the plan. Instead the machinery underneath it gets rebuilt: its one-line translator means turnToHeading keeps working without a single edit. runRepeatedly is the same helper driveWithJoystick used back in Lesson 2 — a plain block of code, run once per tick until something cancels the command.

## Slide 10
SECTION 4 CONTINUED · DRIVETRAIN.JAVA
The last hand-rolled wrap retires
Replace headingError's body with
private double headingError(double targetDegrees) {
return MathUtil.inputModulus(targetDegrees - getHeadingDegrees(), -180, 180);
}
Delete from Drivetrain's imports
import java.util.function.DoubleSupplier; // only translate used it, and it's gone
While you're in the file, headingError gets the same one-liner treatment setDesiredState got in section 3 — its two while loops were the last hand-rolled wrap left in the codebase.
LEARN JAVA + ROBOT PROGRAMMING · FULL SWERVE
10
Notes: headingError's two while loops collapse into the same MathUtil.inputModulus one-liner setDesiredState got in section 3 — the wrap-loop story that ran hand-rolled since Lesson 5 finally retires everywhere it appeared in Drivetrain. The DoubleSupplier import was only there for translate, which is gone now that drive() takes typed LinearVelocity/AngularVelocity suppliers instead of bare doubles — leaving it in place would be a dead import the compiler quietly tolerates but a careful reader would notice.

## Slide 11
SECTION 5 · OPTIMIZE
Steer the short way, every time
Wheel at 10°, told to go to 190°.
It's much faster to steer to 10° and drive at -2 m/s than to physically turn 180°. optimize picks the shorter steering move, flipping the drive sign if needed.
It returns a new value — nothing changes in place.
states[i].optimize(...) alone does nothing — the loop must read states[i] = states[i].optimize(...). Throw away the result and the module gets commanded un-optimized, silently.
LEARN JAVA + ROBOT PROGRAMMING · FULL SWERVE
11
Notes: Without optimize, wheels routinely make 180° pirouettes for no reason, which looks awful and burns time. With it, they nudge a few degrees and reverse — as swerve robots should. Note what it needs to decide: the wheel's current angle — that's why the measurement gets passed in. Worth naming the connection to Lesson 9's cosine trick: optimize keeps every steering move under 90°, which means the cosine scale in setDesiredState never goes negative — the two together give wheels that take the short path AND hold their push until they're pointed right.

## Slide 12
SECTION 6 · ROBOTTELEOP.JAVA
Left stick translates, right stick rotates
Delete the old bindings, add to RobotTeleop's constructor
robot.drivetrain.setDefaultCommand(robot.drivetrain.drive(
() -> DriveConstants.kMaxSpeed.times(-robot.driverController.getLeftY()),
() -> DriveConstants.kMaxSpeed.times(-robot.driverController.getLeftX()),
() -> DriveConstants.kMaxAngularSpeed.times(-robot.driverController.getRightX())));
kMaxSpeed.times(fraction) scales the measure, stays a LinearVelocity.
No maxMps local, no .in(...) — the unit rides all the way from the constant into ChassisVelocities. No boundary to convert at until Phoenix's setThrottle, deep inside setDesiredState.
LEARN JAVA + ROBOT PROGRAMMING · FULL SWERVE
12
Notes: Two edits: delete the Lesson 7 default translate binding and both bumper rotate bindings — those factories no longer exist, and the right stick is taking over rotation. The turnToHeading bindings from Lesson 8 stay; they never stopped working. Look at each supplier: the stick reads a fraction from -1 to 1, and kMaxSpeed.times(fraction) scales the max-speed measure down to that fraction — the result is still a LinearVelocity, exactly what drive now asks for. No maxMps local, no .in(...) — the unit rides all the way from the constant into ChassisVelocities. This is the Units payoff: because every hop speaks the type, there's simply no boundary to convert at until Phoenix's setThrottle, deep inside setDesiredState. Once wired, open the Swerve tab and push both sticks: with ModuleStates and DesiredModuleStates both dropped into the States slots, you see two sets of arrows — where the wheels are told to be, and where they actually are. When the two sets track each other closely, steering control is keeping up; when they lag apart, that's exactly what to tune.

## Slide 13
SECTION 7 · DRIVETRAIN.JAVA
Forward always means away from the driver
Add to Drivetrain
public Command driveFieldRelative(
Supplier<LinearVelocity> vx, Supplier<LinearVelocity> vy, Supplier<AngularVelocity> omega) {
return runRepeatedly(() -> {
ChassisVelocities fieldSpeeds = new ChassisVelocities(vx.get(), vy.get(), omega.get());
Rotation2d heading = Rotation2d.fromDegrees(getHeadingDegrees());
applyChassisSpeeds(fieldSpeeds.toRobotRelative(heading));
}).named("Drive Field Relative");
}
Swap drive for driveFieldRelative in setDefaultCommand — same three suppliers, new method name
robot.drivetrain.setDefaultCommand(robot.drivetrain.driveFieldRelative(
() -> DriveConstants.kMaxSpeed.times(-robot.driverController.getLeftY()),
() -> DriveConstants.kMaxSpeed.times(-robot.driverController.getLeftX()),
() -> DriveConstants.kMaxAngularSpeed.times(-robot.driverController.getRightX())));
LEARN JAVA + ROBOT PROGRAMMING · FULL SWERVE
13
Notes: Right now the sticks are robot-relative: pushing forward always drives the robot in its own forward direction, wherever it happens to be pointing — which means after a 180° turn, forward is backward and half the drivers' brains melt. Most drivers prefer field-relative: pushing forward always drives away from the driver's station, regardless of robot orientation. Thanks to applyChassisSpeeds, this is now a genuinely small method — one new line of math and a delegation. fieldSpeeds.toRobotRelative(...) rotates the field-frame velocity into the robot's frame using the current heading — the gyro from Lesson 8 quietly becoming load-bearing. toRobotRelative reads the same way optimize and cosineScale do: it doesn't change fieldSpeeds, it returns the converted value. Everything downstream still speaks robot frame, and applyChassisSpeeds neither knows nor cares where the speeds came from — that's the extraction paying rent already. Once you feel field-relative driving, you won't want to give it up — that's worth saying plainly, it's the version drivers actually want.

## Slide 14
BEFORE YOU MOVE ON
Try it
1
Watch a wheel optimize
Drive slow forward, then abruptly reverse. The wheel should flip drive sign, not spin 180°.
2
Spin-while-driving auto
WRITE CODE
drivetrain.drive(...) forward at 1 m/s while spinning half a turn per second, for 2 seconds.
3
Slow-mode multiplier
WRITE CODE
While a bumper is held, multiply the three suppliers' outputs by 0.25 for fine control.
LEARN JAVA + ROBOT PROGRAMMING · FULL SWERVE
14
Notes: The watch-a-wheel-optimize exercise is the one worth actually running: drive slow forward, then abruptly reverse, and watch DesiredModuleStates's arrows flip length-direction instead of swinging 180° — that's optimize doing its job visibly, not just in theory. The spin-while-driving auto is a good concrete demonstration that this really is full swerve now — forward motion and rotation composed in one command, which was impossible before this lesson; that one is real code the student writes and drops into Autos. The slow-mode multiplier is a light reprise of composing a new command around drive(...), similar in spirit to Lesson 2's slow-mode Try It but now scaling three suppliers instead of one — also real code, a new command the student writes from scratch.

## Slide 15
WHAT YOU LEARNED
A translation exercise, in the end
ChassisVelocities says what you want; SwerveDriveKinematics translates it into per-wheel SwerveModuleVelocitys.
desaturateWheelVelocities preserves the motion's shape when you overask; optimize trades a pirouette for a sign flip.
Because every path funnels through applyChassisSpeeds, field-relative driving cost one line.
NEXT
Lesson 11
Odometry & Field View
The robot can move any way you ask — now it learns where it is.
LEARN JAVA + ROBOT PROGRAMMING · FULL SWERVE
15
Notes: Full swerve turned out to be a translation exercise: ChassisVelocities says what you want the whole robot to do, SwerveDriveKinematics translates that into per-wheel SwerveModuleVelocitys, and the two hand-rolled commands from Lessons 7–8 collapsed into one drive that mixes translation and rotation freely. One library tool also graduated: MathUtil.inputModulus retired the wrap loop, the same trade the hand-rolled clamp didn't get to make, because this alpha never shipped one to graduate to. The quieter thread running through the whole lesson: optimize, cosineScale, and toRobotRelative all share a shape — call them, get a new value back, original untouched — the same immutable style Rotation2d and Translation2d have had all along, now showing up in the kinematics types too. Field-relative is the version drivers will never let you take away. One thing is still missing: the robot can move any way you ask, but it has no idea where it is. A future lesson gives it a map.