## Slide 1
LEARN JAVA + ROBOT PROGRAMMING
LESSON 16
Ground Truth
Give the simulation a body, and a second truth to check
WPILib 2027 Alpha · Commands V3
Notes: Every pose this course has drawn has been odometry's own estimate, checked against nothing but itself. Today the simulation gets a real chassis body — mass-equivalent grip, a real acceleration limit, a heading tracked once instead of trusted from four separate encoders — and for the first time there's a second, independent truth to compare the estimate against.

## Slide 2
THE GOAL
One shared chassis, instead of four lonely motors
Replace four drive motors that don't know about each other with one shared chassis body that follows its wheels only as hard as its tires can grip — and use it to check odometry against something other than itself for the first time.
NEW JAVA CONCEPTS
None this lesson. Every tool below — private helper methods, a shared static field, if/else if/else — is one you already have. The new ideas are all about the robot, not the language.
NEW ROBOT CONCEPTS
Ground truth — a second, independent "where"
Friction-limited acceleration: a = μg
MathUtil.slewRateLimit — bounding a 2D magnitude
Twist2d.exp() — exact pose integration
LEARN JAVA + ROBOT PROGRAMMING · GROUND TRUTH
2
Notes: No new Java syntax this lesson — the new ideas are all about the robot, not the language.

## Slide 3
SECTION 1 · THE PICTURE WORTH CORRECTING
Your simulation does not model your robot
It models eight motors, each in its own private universe
Four drive motors and four steering motors, each spinning a small flywheel, each unaware anything else exists. Module 0 has never once known module 1 is bolted to the same frame. The chassis has no mass. The tires have no grip.
You've gotten away with it — until now
Every wheel spins exactly as fast as it's told, so odometry has never once been wrong in simulation — just a precise record of what the motors did, with nothing independent to compare it to.
LEARN JAVA + ROBOT PROGRAMMING · GROUND TRUTH
3
Notes: Lesson 15's Try It asked you to give the simulated camera a shaky hand, and the estimate drifted off with nothing to pull it back, because there was no independent truth for vision to be right about. Today that changes: one shared chassis gets a body, and for the first time the number your odometry reports is no longer the only version of events. The best part is what doesn't change: SwerveModule, ModuleIOTalonFX, ModuleIOSim, Localizer, every command, every log key from Lessons 13-15 stay untouched — this all happens in one new class and two small edits, the IO layer from Lesson 13 doing exactly the job it was built for.

## Slide 4
SECTION 2 · THE PHYSICS IN ONE LINE
Grip decides the limit — mass cancels right out
F = μmg
a = F / m
a = μg
The mass cancels — a heavier robot isn't slower to accelerate
The force a tire can supply before skidding is μmg — grip times mass times gravity. Divide by mass for acceleration and the mass drops out entirely: a = μg. That's exactly why real FRC robots don't scale wheel count or tire pressure down just because they're light. Grip alone decides how hard you can accelerate.
LEARN JAVA + ROBOT PROGRAMMING · GROUND TRUTH
4
Notes: Worth sitting with because the answer is smaller than it looks — mass cancels, provided the heavier robot has proportionally more grip to move that weight.

## Slide 5
SECTION 2 · CONSTANTS.JAVA
Four constants: grip, the two acceleration limits, a starting pose
Add to DriveConstants in Constants.java
// How hard the tires can grip, in sim — a Colson-wheel-on-carpet guess.
public static final double kWheelCoF = 1.2;
// a = μg — how hard the chassis can actually accelerate, independent
// of mass, because a heavier robot needs proportionally more force to
// move and proportionally more grip to supply it.
public static final double kMaxAccelMps2 = kWheelCoF * 9.81;
// The same grip limit, applied at each wheel's distance from center.
public static final double kMaxAngularAccelRadPerSec2 =
kMaxAccelMps2 / Math.hypot(kHalfLength, kHalfWidth);
/** Where the simulated robot is placed on the field at startup. */
public static final Pose2d kSimStartingPose = new Pose2d(3, 3, new Rotation2d());
LEARN JAVA + ROBOT PROGRAMMING · GROUND TRUTH
5
Notes: kMaxAngularAccelRadPerSec2 reuses the same idea sideways: a wheel turning the chassis in place traces a circle of radius Math.hypot(kHalfLength, kHalfWidth) — the corner-to-center distance you've had since Lesson 7 — bound by the same μg limit. Add import org.wpilib.math.geometry.Pose2d and import org.wpilib.math.geometry.Rotation2d to Constants.java — the first time this file has needed either.

## Slide 6
SECTION 3 · A NEW FILE
ChassisSimulation — state and construction
Create src/main/java/first/robot/subsystems/ChassisSimulation.java — piece 1
package first.robot.subsystems;
import org.wpilib.math.geometry.Pose2d;
import org.wpilib.math.geometry.Translation2d;
import org.wpilib.math.kinematics.ChassisVelocities;
import org.wpilib.math.util.MathUtil;
import first.robot.Constants.DriveConstants;
public class ChassisSimulation {
private Pose2d m_pose;
private ChassisVelocities m_velocity = new ChassisVelocities();
public ChassisSimulation(Pose2d startingPose) {
m_pose = startingPose;
}
LEARN JAVA + ROBOT PROGRAMMING · GROUND TRUTH
6
Notes: Two fields, and notice what's not here: no per-wheel state at all. This class doesn't know or care how the chassis is being driven — only what velocity it's chasing and where that velocity has carried it. Ground truth — the Drivetrain's own estimate is still built from wheel encoders alone, and the two disagree exactly when the wheels slip, the way they would on a real robot.

## Slide 7
SECTION 3 · A NEW FILE
ChassisSimulation — one tick, following the wheels
Add to ChassisSimulation — piece 2
/** Advance the chassis by one tick, following 'wheels' as closely as grip allows. */
public void update(ChassisVelocities wheels, double dtSeconds) {
Translation2d nextVelocityXY = MathUtil.slewRateLimit(
new Translation2d(m_velocity.vx, m_velocity.vy),
new Translation2d(wheels.vx, wheels.vy),
DriveConstants.kMaxAccelMps2,
dtSeconds);
double omega = chaseOmega(m_velocity.omega, wheels.omega, dtSeconds);
m_velocity = new ChassisVelocities(nextVelocityXY.getX(), nextVelocityXY.getY(), omega);
// Exact integration: how far a constant twist carries the chassis,
// curved turns included, not just a straight-line approximation.
m_pose = m_pose.plus(m_velocity.toTwist2d(dtSeconds).exp());
}
LEARN JAVA + ROBOT PROGRAMMING · GROUND TRUTH
7
Notes: MathUtil.slewRateLimit(current, target, maxRate, dt) moves current toward target, never faster than maxRate per second.

## Slide 8
SECTION 3 · READING THE CODE
A vector rate limit, not two separate ones
Handing it a Translation2d instead of a bare number is the whole trick
vx and vy don't get clamped separately — they're bundled into one 2D vector and rate-limited as a magnitude, so a diagonal acceleration is limited by the same grip a straight-line one is, not double-counted on each axis.
A geometry type, repurposed to hold a velocity
Translation2d is just an (x, y) pair. Nothing stops you from repurposing it to hold a velocity instead of a position — this is a legitimate use of one.
LEARN JAVA + ROBOT PROGRAMMING · GROUND TRUTH
8
Notes: omega has no vector to join, so it gets a small helper of its own — the scalar sibling of slewRateLimit, written by hand because the library only ships the vector version.

## Slide 9
SECTION 3 · A NEW FILE
ChassisSimulation — chaseOmega, and a getter
Add to ChassisSimulation — piece 3, closing out the class
/** Move 'current' toward 'target', never faster than the grip-limited angular rate. */
private double chaseOmega(double current, double target, double dtSeconds) {
double maxStep = DriveConstants.kMaxAngularAccelRadPerSec2 * dtSeconds;
double error = target - current;
if (error > maxStep) {
return current + maxStep;
} else if (error < -maxStep) {
return current - maxStep;
} else {
return target;
}
}
public Pose2d getPose() {
return m_pose;
}
}
LEARN JAVA + ROBOT PROGRAMMING · GROUND TRUTH
9
Notes: Read that as the scalar sibling of slewRateLimit — same idea, one number instead of two.

## Slide 10
SECTION 3 · READING THE CODE
Twist2d.exp() — the same math odometry runs internally
toTwist2d(dt) — "this velocity, held for this long"
m_velocity.toTwist2d(dtSeconds) turns a velocity into a Twist2d — how far the chassis moved in that instant, exactly the small nudge SwerveDriveOdometry computes every tick from your wheel encoders.
exp() turns that nudge into a curve, not a straight line
Twist2d.exp() accounts for the curve a turning chassis actually traces, and Pose2d.plus(Transform2d) composes it onto where the chassis already was — precisely what SwerveDriveOdometry.update(...) does under the hood, written out instead of hidden behind a library call.
LEARN JAVA + ROBOT PROGRAMMING · GROUND TRUTH
10
Notes: You're not approximating anything here — this is exact pose integration, curved turns included.

## Slide 11
SECTION 4 · DRIVETRAIN.JAVA
One shared chassis, null on a real robot
Add to Drivetrain, above the m_gyroIO field
// The chassis's ground truth in the physics world — one, shared, null on
// a real robot (which already has a world) and in replay (which needs none).
private static final ChassisSimulation m_chassisSim = createChassisSim();
Add the builder, next to makeModule
/** Builds the shared chassis ground truth. Sim only — null everywhere else. */
private static ChassisSimulation createChassisSim() {
if (Constants.kCurrentMode != Constants.Mode.SIM) {
return null; // a real robot already has a world; replay doesn't need one
}
return new ChassisSimulation(DriveConstants.kSimStartingPose);
}
LEARN JAVA + ROBOT PROGRAMMING · GROUND TRUTH
11
Notes: ChassisSimulation needs exactly one home: shared by every module (they're all bolted to the same frame), null on a real robot and in replay — the same shape Lesson 13's ModuleIO/GyroIO switch expressions already taught you to reach for.

## Slide 12
SECTION 4 · DRIVETRAIN.JAVA
Move the chassis the way its wheels actually turned
Register a second periodic in Drivetrain's constructor, below the first
public Drivetrain() {
Scheduler.getDefault().addPeriodic(this::periodic);
Scheduler.getDefault().addPeriodic(this::simulateChassis);
}
Add the method, next to periodic()
/** Moves the simulated chassis the way its wheels actually turned this tick. Sim only. */
private void simulateChassis() {
if (m_chassisSim == null) {
return; // a real robot moves itself
}
SwerveModuleVelocity[] wheels = new SwerveModuleVelocity[4];
for (int i = 0; i < m_modules.length; i++) {
wheels[i] = new SwerveModuleVelocity(
m_modules[i].getDriveVelocityMetersPerSec(),
Rotation2d.fromDegrees(m_modules[i].getSteerAngleDegrees()));
}
m_chassisSim.update(m_kinematics.toChassisVelocities(wheels), 0.020);
}
LEARN JAVA + ROBOT PROGRAMMING · GROUND TRUTH
12
Notes: Move it how much? Not as much as you asked the wheels to — as much as the wheels actually turned. A robot can't outrun its own wheels. What it can do is fall short of them: ask the tires for more than they can grip and the wheels spin faster than the chassis moves. That's slip, and it's exactly the gap the grip limit in ChassisSimulation creates. Watching the wheels is a job for every tick, whether a command is running or not — the same kind of job periodic() does — so it gets a periodic callback of its own. toChassisVelocities runs kinematics backward: four wheel velocities in, the one chassis velocity they add up to out — the reverse of the toSwerveModuleVelocities call applyChassisSpeeds has made since Lesson 10.

## Slide 13
SECTION 4 · DRIVETRAIN.JAVA
Delete the fake gyro's feeds, then expose the truth
DELETE from inside applyChassisSpeeds
// nothing integrates a commanded rate by hand anymore; the shared
// chassis tracks heading itself now.
m_gyroIO.setSimRotationRate(speeds.omega / (2 * Math.PI));
DELETE from driveDistance, where it zeroed the rate
m_gyroIO.setSimRotationRate(0.0);
Add next to getHeadingDegrees()
/** Where the chassis really is, ground truth — null outside sim. */
public Pose2d getSimulatedPose() {
return m_chassisSim != null ? m_chassisSim.getPose() : null;
}
LEARN JAVA + ROBOT PROGRAMMING · GROUND TRUTH
13
Notes: Two small deletions retire the fake gyro's bookkeeping, and one getter exposes the truth so the rest of the file — and Lesson 15's cameras — can reach it.

## Slide 14
SECTION 5 · A REWRITTEN FILE
The gyro stops pretending, and just reads the truth
Replace the whole contents of GyroIOSim.java
package first.robot.subsystems;
/** Reports the heading of the real simulated chassis — no integration of its own. */
public class GyroIOSim implements GyroIO {
private final ChassisSimulation m_chassisSim;
public GyroIOSim(ChassisSimulation chassisSim) {
m_chassisSim = chassisSim;
}
@Override
public void updateInputs(GyroIOInputs inputs) {
inputs.yawDegrees = m_chassisSim.getPose().getRotation().getDegrees();
}
}
LEARN JAVA + ROBOT PROGRAMMING · GROUND TRUTH
14
Notes: Lesson 8 gave you a fake gyro that integrated the rotation rate you commanded — add omega × dt every tick and call it a heading. It was a reasonable lie with a tell: a robot commanded to spin always spun exactly as asked, with no acceleration limit slowing it down. The chassis sim you just built already tracks heading properly, grip limit and all — the gyro should just read it.

## Slide 15
SECTION 5 · GYROIO.JAVA + DRIVETRAIN.JAVA
A dead method, deleted — and the gyro gets its chassis
DELETE from the GyroIO interface
// nothing integrates a commanded rate anymore; the shared chassis
// tracks rotation and the gyro just reports it.
public default void setSimRotationRate(double omegaRevPerSec) {}
Edit the gyro switch in Drivetrain
private final GyroIO m_gyroIO = switch (Constants.kCurrentMode) {
case REAL -> new GyroIOPigeon2();
case SIM -> new GyroIOSim(m_chassisSim);
case REPLAY -> new GyroIO() {}; // inputs come from the log
};
LEARN JAVA + ROBOT PROGRAMMING · GROUND TRUTH
15
Notes: That deletion has a tail, and it's the good kind: nothing anywhere calls setSimRotationRate anymore, so the method itself is dead.

## Slide 16
SECTION 5 · WHY THE ORDER MATTERS
Field initializers run top to bottom
This is exactly why m_chassisSim had to come first
GyroIOSim's constructor needs a chassis that already exists. Because m_chassisSim was declared above m_gyroIO back in section 4, it's already built by the time the gyro field's initializer runs — the same ordering discipline Lesson 14 taught you with m_drivetrain before m_localizer.
LEARN JAVA + ROBOT PROGRAMMING · GROUND TRUTH
16
Notes: Field declaration order isn't cosmetic — it's the sequence Java actually runs the initializers in.

## Slide 17
SECTION 6 · DRIVETRAIN.JAVA
Publish the truth, alongside the estimate
Log it at the end of periodic()
if (m_chassisSim != null) {
Telemetry.log("Drivetrain/SimulatedPose", m_chassisSim.getPose(), Pose2d.struct);
}
}
The same Telemetry.log call that publishes Drivetrain/Heading a few lines up — handed a Pose2d and its .struct this time.
LEARN JAVA + ROBOT PROGRAMMING · GROUND TRUTH
17
Notes: Every pose this course has drawn has been an estimate. That's no longer true — the chassis sim tracks where the chassis actually is, independent of what any wheel reports, and it's been running since section 4.

## Slide 18
SECTION 6 · DRIFT YOU DIDN'T HAVE TO FAKE
Drive hard, and watch the two poses separate
1
AdvantageScope → Odometry tab
Put both Localizer/Pose and Drivetrain/SimulatedPose on the field at once.
2
Drive gently
The two poses sit right on top of each other.
3
Drive like you mean it
Full stick from a stop, a hard reversal, a fast spin — watch them separate.
4
The estimate creeps ahead, and stays there
Nothing resets it — addition never forgets.
LEARN JAVA + ROBOT PROGRAMMING · GROUND TRUTH
18
Notes: The wheel motors respond to a velocity command quickly (Lesson 12's firmware loop doing its job); the chassis is limited by the same grip you just gave it a number for. When you ask for more than the tires could really deliver, the wheels report motion that never fully became chassis motion, odometry counts every rotation as if it had, and the estimate creeps ahead of the truth — precisely the argument Lesson 14 opened with, except this time you're watching it happen instead of taking its word.

## Slide 19
SECTION 7 · ROBOT.JAVA
Closing the loop: vision checks itself against truth
Change both camera suppliers in Robot's constructor
frontCamera = LimelightPoseProvider.makeCamera(
VisionConstants.kFrontCameraName, VisionConstants.kFrontRobotToCamera,
drivetrain::getSimulatedPose);
backCamera = LimelightPoseProvider.makeCamera(
VisionConstants.kBackCameraName, VisionConstants.kBackRobotToCamera,
drivetrain::getSimulatedPose);
That's the whole fix — drivetrain::getSimulatedPose in place of localizer::getPose. The simulated camera now renders from where the chassis actually is, so a correction it computes pulls the estimate toward something real, not toward itself.
LEARN JAVA + ROBOT PROGRAMMING · GROUND TRUTH
19
Notes: Lesson 15 admitted a compromise: VisionIOLimelightSim looked out from localizer::getPose — the very estimate vision was supposed to correct — because no independent truth existed yet. One does now, and the fix is a one-line swap.

## Slide 20
SECTION 7 · ROBOT.JAVA
One loose end: tell the estimate where it started
Add to Robot's constructor, after the cameras are registered
// The simulated chassis starts at kSimStartingPose; tell the estimate
// where that is instead of guessing from (0, 0, 0°).
if (Constants.kCurrentMode == Constants.Mode.SIM) {
localizer.resetPose(DriveConstants.kSimStartingPose);
}
The chassis sim starts at kSimStartingPose, but Localizer still starts at (0, 0, 0°), because odometry has no idea where it was switched on. Left alone, you'd watch two robots in different places and doubt your own code.
LEARN JAVA + ROBOT PROGRAMMING · GROUND TRUTH
20
Notes: A one-time correction, guarded by SIM, so a real robot's boot-time pose is left exactly as it was.

## Slide 21
RUN IT
Feel the grip limit, then watch vision pull the estimate home
1
./gradlew simulateJava → RobotTeleop
Push the stick to full — the robot ramps up, the way a real chassis with real tires does.
2
Let go of the stick
It coasts back down instead of stopping dead.
3
Drive hard enough to separate the two poses
The way section 6 showed you, then park somewhere a tag is visible.
4
Watch Localizer/Pose get pulled back
Toward Drivetrain/SimulatedPose — odometry for smoothness, vision for truth.
LEARN JAVA + ROBOT PROGRAMMING · GROUND TRUTH
21
Notes: For the first time, a truth to compare against instead of a guess checking itself.

## Slide 22
BEFORE YOU MOVE ON
Try it
1
Slicker tires
WRITE CODE
Drop kWheelCoF to 0.4 and repeat hard driving. The estimate should peel away from ground truth far faster. Put it back — and if Lesson 13's Try It left a fake 1.1 wheel-slip multiplier in ModuleIOTalonFX, delete it now.
2
Spin, not just a line
Command a fast turnToHeading from a stop and compare Drivetrain/Gyro/YawDegrees against how fast the raw commanded rate would have turned the robot with nothing limiting it.
LEARN JAVA + ROBOT PROGRAMMING · GROUND TRUTH
22
Notes: Item 1 is a real code edit — and a cleanup, if an earlier Try It left a fake wheel-slip multiplier behind. Item 2 is an observe-and-compare exercise — no code changes, just watching the gyro visibly lag the instant command, something Lesson 8's fake gyro could never have shown you because it had no concept of "too fast to actually achieve."

## Slide 23
BEFORE YOU MOVE ON
Try it, continued
3
Push the estimate somewhere wrong on purpose
WRITE CODE
Call m_localizer.resetPose(...) from a temporary button binding, half a meter off from the chassis sim, then park where a tag is visible. Watch the estimate get pulled back — toward the truth this time.
LEARN JAVA + ROBOT PROGRAMMING · GROUND TRUTH
23
Notes: Item 3 is a real code edit, and the payoff of the whole lesson: until now vision could only pull the estimate toward the estimate itself. With the camera rendering from ground truth, a deliberately wrong estimate gets pulled back toward where the robot actually is.

## Slide 24
WHAT YOU LEARNED
The simulation finally has a body
One shared chassis, following its wheels under a μg acceleration limit, replaced four drive motors that never knew about each other — and because the limit comes from grip alone, mass canceled right out of the formula.
MathUtil.slewRateLimit on a Translation2d limited acceleration as a true 2D magnitude, and Twist2d.exp() gave you exact pose integration — the same math SwerveDriveOdometry has been running for you since Lesson 11, written out by hand this time.
What's actually worth stopping on: an entire ground-truth chassis went into the project, and SwerveModule never heard about it — Lesson 13's IO-layer boundary made ground truth cheap.
NEXT
Lesson 17
B-Line Autos
An auto drawn as a shape on the field, and a robot that chases it.
LEARN JAVA + ROBOT PROGRAMMING · GROUND TRUTH
24
Notes: And Lesson 15's admitted compromise is gone. Vision checks its simulated eyesight against where the chassis actually is now, not against its own guess — the same one-line supplier swap you'd make to point a real camera at a real robot's real position, because that's what a real camera was doing all along.